## Slide 1: Signal Processing of Geospatial and Biometric Data from Wearable Devices for Fall Detection
Joseph Caguioa, Andy Nguyen, & Michael J. Wolfe

## Slide 2: Motivation
In 2016 falls were the leading cause of injury-related deaths in seniors
  ~30,000 adults 65 years and older experienced fatal falls in 2016 with increasing death rates annually since 2007 in the U.S.
  ~ 646,000 reported globally
Falls are often associated with (strokes) or can result in life-threatening situations (TBI) that require immediate medical intervention for patient’s survival
  Risk factors of advanced age: reduced activity/gait/balance, neurologic disease, other underlying medical conditions
  Other risk factors: hazardous working conditions, substance abuse, socioeconomic factors (World Health Organization)

## Slide 3
How can we optimize health outcomes by quickly diagnosing fall events?

## Slide 4: Research Idea
Use sensor data (accelerometer and gyroscope) from wearable devices to detect falls and immediately dispatch paramedics to device’s GPS location
Algorithm should differentiate between actual falls and false positive events (activities of daily living, intentional falls)
Notes: Waist and head are located on the axis of the human anatomy’s center of gravity

## Slide 5
Waist and head are algorithmically preferred
Wrist is more practical for daily wear

## Slide 6: Past Research
A simple threshold model detects a fall and the results are applied to a Hidden Markov Models to differentiate between an actual fall and an activity of daily living (ADL)
  Fall-Detection Algorithm Using 3-Axis Acceleration: Combination with Simple Threshold and Hidden Markov Model (Dongha Lim, Chulho Park, Nam Ho Kim, Sang-Hoon Kim, Yun Seop Yu): 2014
A simple threshold model is combined with a multiphase fall model (free fall, impact, and rest) as a solution to the technical challenges of differentiating a fall from ADL
  Novel Hierarchical Fall Detection Algorithm Using a Multiphase Fall Model (Chia-Yeh Hsieh, Kai-Chun Liu, Chih-Ning Huang, Woei-Chyn Chu, Chia-Tai Chan): 2017
A 3-tier model architecture combining simple threshold models with machine learning algorithms to detect falls from smartphone sensors implemented in an Android application called uSurvive. The application runs as a background service to monitor activity and can automatically send notifications to authorities when a fall is detected.
  An Energy-Efficient Multi-Tier Architecture for Fall Detection on Smartphones (M. Amac Guvensan, A. Oguz Kansiz, N. Cihan Camgoz, H. Irem Turkmen, A. Gokhan Yavuz, M. Elif Karsligil): 2017

## Slide 7: Models
Our Model Approach:
  Simple Threshold Model
  Multiphase Fall Model
  Test Combination of Different Machine-Learning Algorithms
    Principal Component Analysis
    Linear Discriminant Analysis
    Support Vector Machines
    Hidden Markov Model
    Naïve Bayesian Classifier
    Decision Trees
    Random Forests
  Undifferentiated Range of ADL as majority response

## Slide 8: Potential Challenges
Wearable devices are the most common application of past algorithms
Single sensor placement limits the amount of spatial data that can be processed
Multiple sensors are more effective but less practical
Manufacturers of devices are protective of their data and algorithms

## Slide 9: Questions?